## Slide 1: Queue-Proportional Sampling: A Better Approach to Crossbar Scheduling for Input-Queued Switches
Presenter: Long Gong
Advisor: Jun (Jim) Xu
Notes: Good afternoon, professors. I am Long Gong, and my advisor is Prof. Jim Xu.
Today, my topic is Queue- …
There are five parts in my presentation.

## Slide 2: Contents
Background
1
Related Work
2
Proposed Algorithm
3
Simulation Results
4
Miscellaneous
5
Notes: In the first part, I will give some background on input-queued crossbar switches. Then we will talk about some related work. After that, I will describe the details of queue-proportional sampling scheme, followed by some simulations results. Finally, I will summarize this presentation. First, Let’s come into the background part.

## Slide 3: Contents
Background
1
Related Work
2
Proposed Algorithm
3
Simulation Results
4
Miscellaneous
5

## Slide 4: Input-Queued Crossbar Switches
Segment
Crossbar
VOQ 1
VOQ N
VOQ 1
VOQ N
Input 1
Input N
Output N
Output 1
Segment
Assemble
Assemble
Segment variable-size packets into fixed-size
Reassemble packets before they leave
Packets
Notes: Nowadays, most high-speed switching systems, such as Internet routers and data-center switches, employ a single crossbar to interconnect input ports and output ports.
To solve the HOL blocking issue, each input port has N virtual output queues (VOQs). The VOQ j at input port I serves as a buffer for packets going from input port I to output port j.
For example, here the VOQ 1 at input port 1 buffers the packets that want to go from input port 1 to output port 1.
In this work, we also adopt the standard assumption. That is all incoming packets are segmented into fixed-size before they are put into the corresponding VOQs and then reassembled
Before leaving the switch.

## Slide 5: Scheduling for Input-Queued Crossbar Switches
Input 1
Input 2
Input N
Output 1
Output 2
Output N
?
Which input connects to which output?
Abstraction
Constraints (Physical Limits of the Crossbar)
Each input can only connect to a single output
Each output can only be connected by a single input
Crossbar
VOQ 1
VOQ N
VOQ 1
VOQ N
Input 1
Input N
Output N
Output 1
Notes: Due to the physical limits of a crossbar fabric, in an input-queued switch, each input port can only connect to a single output port and vice versa in each switching cycle, or time slot.
Hence, input-queued switches need to decide which input port connects to which output port per time slot. More specially, they need to compute a one-to-one matching between input ports and output ports

## Slide 6: Scheduling for Input-Queued Crossbar Switches: Formulation
Input 1
Input 2
Input N
Output 1
Output 2
Output N
Problem: Compute a one-to-one matching between input and output ports
Model: Weighted Complete Bipartite Graph
Challenge: “high quality” matchings (i.e., high through-put & low delay) at high speed
Quality of the matching
Time to compute the matching
Notes: Generally, a NXN crossbar switch is modeled as a weighted bipartite graph, where the two disjoint sets of vertices are the input ports and output ports, respectively. The weight is some function of the length of the corresponding VOQs.
The problem is to compute high-quality matchings that result in high switch throughput and low delay at high speed.
Unfortunately, there exists a tradeoff between the quality of the matchings and the time to compute them.

## Slide 7: Contents
Background
1
Related Work
2
Proposed Algorithm
3
Simulation Results
4
Miscellaneous
5
Notes: Next, let’s see some related work.

## Slide 8: Existing Scheduling for Input- Queued Crossbar Switches
Quality of the matching
Time to compute the matching
Maximum Weighted Matching (MWM)
Serena [Giaccone03]
iSLIP [McKeown99]
Quality of the matching
Time to compute the matching
Empirically optimal
Optimal throughput
Quality of the matching
Time to compute the matching
Good delay performance
Notes: Now, let’s see how the tradeoff was handled in existing work.
Maximum Weighted Matching with suitable weight measure, is known to produce the empirically optimal matchings in terms of queuing delay for a large variety of traffic patterns. However, each such matching decision takes O(N^3) time to compute, which is too time-consuming to be used. Researchers have been searching for alternatives that have performance close to MWM but with much lower time complexity.
iSLIP is one such algorithm, which is an iterative algorithm with good delay performance. It has a per-port complexity of (log N)^2 (log N iterations with each iteration having O(log N) circuit depth). Although it achieved great commercial success, iSLIP generally can not achieve 100% except under uniform traffic, thus it could have very high delay even infinite delay under heavy non-uniform traffic.
Serena is also such algorithm, which is a centralized algorithm with linear time complexity . It can achieve 100% throughput and excellent delay performance.

## Slide 9: Why Need New Scheduling Algorithms
Switches Can Connect A Large Number of Ports and Operate at Very High Speed
Quality of the matching
Time to compute the matching
Achieve Better Tradeoff
Reality
Badly Need
K ports & Tb/s in the future [DeCusatis2013]
Improve
Decrease
Notes: You might be wondering why we still need to design new scheduling algorithms considering we already have such good ones like iSLIP and Serena.
Thanks to the big success of Big Data, video streaming, online social networking, and etc, the volumes of network traffic are growing relentlessly.
Driven by the surge of the traffic, it is expected that a switch would have more than 1000 ports and the line rate of each port could be larger than 1 Tb/s.
Therefore, switches that are capable of connecting a large number of ports and operating at very high speed is badly needed.
In this work, we aim at achieving better tradeoff. Clearly, we can either improve the quality of the matchings or decrease the computational complexity. In this work, we proposed a solution to improve the performance with very low computational overhead.

## Slide 10: Contents
Background
1
Related Work
2
Proposed Algorithm
3
Simulation Results
4
Miscellaneous
5
Notes: Now, Let’s see how our scheme works.

## Slide 11: Queue-Proportional Sampling (QPS): Overview
Proposing (at any input port)
Accepting (at any output port)
Step 1: Sample an output port with probability
Step 2: Send to output port (assume is sampled is Step 1)
: length of the VOQ
: total length of VOQs
Accept the one with the largest VOQ length if receiving one or more proposals
Note that, besides the “longest VOQ first” accepting strategy, we also investigate “proportional” accepting
Notes: Our strategy is called Queue-proportional sampling, which is a general add-on approach to boost the performance of existing scheduling algorithms, such as iSLIP and Serena.
This strategy is extremely simple. It has two stages. The first one is called proposing. In this stage, each input port first samples out an output port with the probability proportional to the corresponding VOQ length, then the input port sends a proposal requests together with the VOQ length to the output port that is sampled.
The second stage is accepting. In this stage, each output port upon receiving one or more proposals, it accepts the one with the largest VOQ length. Note that, besides the “longest VOQ first”, we also investigate other accepting strategies, such as proportional accepting.

## Slide 12: Queue-Proportional Sampling (QPS): Example
VOQ ID | VOQ Length
1 | 3
2 | 7
3 | 6
4 | 2
3
7
6
2
Sample a VOQ
Proposals | 
Input ID | VOQ Length
1 | 3
4 | 1
Crossbar
VOQ 1
VOQ 4
VOQ 1
VOQ 4
Input 1
Input N
Output 4
Output 1
Notes: Now, let’s see a concrete example, with N=4. For the proposing, let’s focus on input port 1, the lengths of all VOQs are shown in the table.
First of all, it samples out a output port with probability proportional to the corresponding VOQ lengths. It samples output 1. Then, it sends the length of VOQ 1 to output 1.
For the accepting, let’s focus on output 1, assuming besides the proposal from input port 1, it also gets a proposal from input port 4. Output 1 accepts the proposal from input port 1, since it has a longer VOQ.

## Slide 13: Queue-Proportional Sampling (QPS): O(1) Data Structure
“Packets” in All of VOQs at Input Port i
VOQs at Input Port i
VOQ j
B | j | 
E | j | 
A | j | 
F | j | 
G |  | B |  | A |  | C | D
Main Data Structure
Array of linked lists
Each link list => VOQ
Auxiliary Data Structure
Array of all packets
One-to-one correspondence
Notes: It may look at first that one may need up to O(N) time complexity to finish the QPS. However, it is possible to implement QPS efficiently with only O(1) time complexity.
Now let’s see the O(1) data structures.
Although the O(1) data structures are fairly simple and straightforward, we did not find any similar ones in the literature.
The data structures have one main data structure and one auxiliary. The main data structure is just an array of linked lists, where each linked list corresponds to a VOQ. Besides the pointers for forming the linked list, each entry in the linked list has a pointer points to the actual packet (shown as a letter), a index recording which VOQ the packet is located. It also holds a pointer that points to the corresponding entry in the auxiliary data structure.
The auxiliary data structure is just one array, where each entry corresponds to a packet in the input port. More specially, each entry in the array is a pointer points to the corresponding entry in the linked list of the corresponding VOQ. Hence there is one-to-one correspondence between entries in the main data structure and the entries in the auxiliary data structure.
Now, we use an example to show how the data structure works. Assume there are q entries in the auxiliary data structure.
First of all, we sample an entry from the auxiliary array by simply generating a uniformly distributed random variable in the range from 0 to q – 1. For example, the entry A is sampled. Then we find the entry in the linked list. However, it is not a head of line packet. We then get the head of line packet of the same VOQ, which is the packet B. Assume the proposal is accepted, which means we need eventually delete entry B from the linked list. Clearly, we also need to remove B from the auxiliary data structure. Now, there comes another problem, we can not afford to move forward all entries after B, however, we can easily fill this hole by moving the last entry into it.
It is clear that all these steps can be finished in O(1) time complexity.

## Slide 14: Queue-Proportional Sampling (QPS): O(1) Data Structure
“Packets” in All of VOQs at Input Port i
VOQs at Input Port i
VOQ j
E | j | 
A | j | 
F | j | 
G |  | D |  | A |  | C
Main Data Structure
Array of linked lists
Each link list => VOQ
Auxiliary Data Structure
Array of all packets
One-to-one correspondence

## Slide 15: QPS-Serena: Overview
Populate the starter matching to a full matching by pairing unmatched input and output ports in a round robin manner
Generate a starter matching with Queue-Proportional Sampling (QPS)
Merge the populated full matching with the matching in previous time slot
Starter Matching
(QPS)
Populate
Merge
Notes: Now, let’s see how our QPS can be used to augment Serena.
First of all, we use QPS to generate a starter matching.
Then, we populate this matching into a full one by pairing all unmatched input ports and output ports in a round-robin manner.
Finally, we merge this full matching with the matching used in previous time slot by cherry-picking heavier edges among the two matchings.

## Slide 16: QPS-Serena: Example
1
2
3
4
1
2
3
4
Starter Matching
Populate
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Matching in Previous Time Slot
Merge
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Pick heavier sub-matching in each cycle
VOQ | Length
(1,1) | 3
(2,2) | 8
(2,4) | 9
(3,2) | 2
(3,3) | 1
(4,3) | 7
(4,4) | 4
Notes: For example, by using QPS, we generate a starter matching. Here, the orange nodes represent the input ports while the green ones stand for output ports.
Then, we populate it into full matching by pairing unmatched input/output ports in a round-robin manner, that is the first unmatched input port pairs with the first unmatched output port, the second with the second, and so on so forth until all ports are matched.
Now, we assume the matching used in the previous time slot looks like this. Then we merge the two full matchings.
The merge procedure works as follows.
It first creates a new bipartite graph by only using edges from the two matchings. It was proven that such a bipartite graph could be decomposed into certain cycles.
And each such cycle contains the same number of edges from the two matchings in an alternating manner. Picking heavier sub-matching in each such cycle finishes the merge procedure.

## Slide 17: Stability of QPS-Serena
Admissible traffic patterns
  : The normalized mean arrival rate of packets to the VOQ at input port .
  The traffic matrix is called admissible if
QPS-Serena can achieve 100% throughput under all i.i.d. admissible traffic arrival process.
Notes: For a scheduling algorithm, the stability is one of the most desired features.
It was proven that Serena is stable under any i.i.d. admissible traffic. Its stability comes from its two properties. Property P and Non-degenerative.
Therefore, there is a positive probability that Serena can achieve the same weights as MWM; and it guarantees that current matchings decision would not be worse that the previous one.
Although QPS-Serena also shares the non-degenerative property, but it generally does not satisfy the property p.

## Slide 18: Contents
Background
1
Related Work
2
Proposed Algorithm
3
Simulation Results
4
Miscellaneous
5
Notes: After talking about the proposed algorithms. Let’s evaluate its performance.

## Slide 19: Simulation Setup
Parameters | Values
N, number of input/output ports | 32
T, number of time slots simulated | 6,000X
Arrival Processes | Bernoulli i.i.d., ON-OFF Bursty
Traffic patterns | uniform, Quasi-diagonal, Log-diagonal, Diagonal
Parameters | Values
N, number of input/output ports | 32
T, number of time slots simulated | 
Arrival Processes | Bernoulli i.i.d., ON-OFF Bursty
Traffic patterns | uniform, Quasi-diagonal, Log-diagonal, Diagonal
Notes: Here are the parameters for our simulations. We simulate 32 times 32 switches. Every simulation run lasts for 6,000 times N square time slots.
We evaluated Bernoulli i.i.d. and ON-OFF bursty arrival processes.
We used four traffic patterns: uniform, quasi-diagonal, log-diagonal and diagonal.

## Slide 20: Mean Delay (Bernoulli i.i.d.)
QPS-Serena vs. Serena
Notes: First, let’s compare the mean delay between QPS-Serena and Serena under Bernoulli i.i.d arrivals. It can be seen that QPS-Serena improves the performance of Serena in huge margins.
In real networks, packet arrivals are more likely to be bursty ….

## Slide 21: Mean Delay (Burst)
QPS-Serena vs. Serena
Notes: This slide shows the mean delay of QPS-Serena and Serena under burst arrivals.
Lower delay
Gap shrinks rapidly

## Slide 22: Contents
Background
1
Related Work
2
Proposed Algorithm
3
Simulation Results
4
Miscellaneous
5
Notes: Finally, let’s summarize this presentation.

## Slide 23: Three types of switching fabrics
This slide was downloaded from Internet!

## Slide 24: Switching Via Memory
First generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
Input
Port
Output
Port
Memory
System Bus
This slide was downloaded from Internet!

## Slide 25: Switching Via a Bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
1 Gbps bus, Cisco 1900: sufficient speed for access and enterprise routers (not regional or backbone)
This slide was downloaded from Internet!

## Slide 26: Switching Via An Interconnection Network
overcome bus bandwidth limitations
Banyan networks, other interconnection nets initially developed to connect processors in multiprocessor
Advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
  Segmentation and Reassembly (SAR)
    Discuss overheads
Cisco 12000: switches Gbps through the interconnection network
This slide was downloaded from Internet!

## Slide 27: Router Architecture Overview
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric
Input Port Functions
This slide was downloaded from Internet!

## Slide 28: Router Architecture Overview
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
Output Ports
This slide was downloaded from Internet!

## Slide 29: Router Architecture Overview
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
Output Port Queuing
This slide was downloaded from Internet!

## Slide 30: Router Architecture Overview
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Input Port Queuing
This slide was downloaded from Internet!

## Slide 31: Head of Line blocking
1
2
3
This slide was downloaded from Internet!

## Slide 32
Virtual Output Queueing
This slide was downloaded from Internet!

## Slide 33: QPS-iSLIP: Overview
QPS
iSLIP (Multiple Iterations)
Request
VOQ
Not
Empty
Grant
Round
Robin
(Grant
pointer)
Accept
Round
Robin
(Accept
pointer)
Input Port
Output Port

## Slide 34: QPS-iSLIP: Example
1
2
3
4
1
2
3
4
Starter Matching
2
2
4
3
3
3
1
4
1
2
3
4
1
2
3
4
2
2
4
3
3
3
1
4
Request
1
2
3
4
1
2
3
4
2
2
4
3
3
3
1
4
Grant
1
2
3
4
1
2
3
4
2
2
4
3
3
3
1
4
Accept

## Slide 35: QPS-iSLIP: Example
1
2
3
4
1
2
3
4
Starter Matching
2
2
4
3
3
3
1
4
1
2
3
4
1
2
3
4
2
2
4
3
3
3
1
4
Request
1
2
3
4
1
2
3
4
2
2
4
3
3
3
1
4
Grant
1
2
3
4
1
2
3
4
2
1
1
3
4
3
1
2
Accept
One More Iteration
1
2
3
4
1
2
3
4
2
1
1
3
4
3
1
2

## Slide 36: Four Traffic Patterns
Uniform
Quasi-diagonal
Log-diagonal
Diagonal
Notes: The traffic patterns

## Slide 37: ON-OFF Bursty Arrivals
ON
OFF
Notes: In an OFF state, an incoming packet’s destination (output port) is generated according to the corresponding traffic pattern. In an ON state, all incoming packet arrivals to an input port would be destined to the same output port thus simulating a burst of packets.
By adjusting p, we can control the desired average burst size; By adjusting q, we can control the load of the traffic.

## Slide 38: Maximum Achievable Throughput
Traffic | Uniform | Quasi-diagonal | Log-Diagonal | Diagonal
iSLIP | 100.00% | 81.70% | 83.85% | 83.47%
QPS-iLSIP | 100.00% | 99.38% | 96.46% | 88.35%
iLQF | 100.00% | 99.41% | 96.47% | 89.32%
0 | 0.1768 | 0.1261 | 0.0489
improvement
QPS-iSLIP vs. iSLIP

## Slide 39: Mean Delay (Bernoulli i.i.d.)
QPS-iSLIP vs. iSLIP

## Slide 40: Mean Delay (Burst)
QPS-iSLIP vs. iSLIP